## Slide 1: Introduction to Transport Layer
Lecture 4 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
Our goals:
understand principles behind transport layer services
learn about two transport layer protocols:
  UDP: User Datagram Protocol
  TCP: Transmission Control Protocol

## Slide 3: Transport vs. Network layer
transport layer: logical communication between processes
network layer: logical communication between hosts
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill
network-layer protocol = postal service
household analogy:
Segments: Transport Layer PDU

## Slide 4: Functions of the Transport Layer
Primary responsibilities:
  Segmenting the data and managing each piece.
  Reassembling the segments into streams of application data.
  Identifying the different applications.
  Multiplexing
  Initiating and terminating a connection.
  Performing flow control between end users.
  Enabling error recovery.
Reliability

## Slide 5: Different Applications
Some applications need their data to be complete with no errors or gaps.
But can accept a slight delay to ensure this.
Some applications can accept occasional errors or gaps in the data.
But they cannot accept any delay.
Different Requirements
Online Games
Emails
Web Applications

## Slide 6: Solution : Two transport protocols?
Emails
Web Applications
Reliable
TCP
Online Games
Fast
UDP

## Slide 7
UDP : User Datagram Protocol
  Best Effort Service
  Used by applications that requires no delay in data delivery
How does UDP deliver fast?
  no connection establishment (which can add delay)
  small header size
  no error or flow or congestion control: UDP can blast away as fast as desired
UDP: User Datagram Protocol [RFC 768]

## Slide 8
UDP is used by:
  streaming multimedia apps (loss tolerant, rate sensitive)
  SNMP
  But sometimes ……
  DNS
  HTTP/3
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!
User Datagram Protocol (UDP)

## Slide 9: Functions of the Transport Layer
Primary responsibilities:
  Segmenting the data and managing each piece.
  Reassembling the segments into streams of application data.
  Identifying the different applications.
  Multiplexing
  Establishing and terminating a connection
  Enabling error recovery.
  Performing flow control between end users.
Only TCP
UDP &TCP

## Slide 10
Function 1&2 – Segmentation and Reassembly

## Slide 11
Function 2 – Reassembly
UDP
TCP

## Slide 12: TCP and UDP Headers
UDP HEADER
TCP HEADER

## Slide 13
TCP Header
UDP Header
TCP and UDP Headers

## Slide 14: Function 3 – Identifying Different Applications
Port Numbers/Addresses are used to identify different applications/processes running in a computer
16-bits in length
  Represented as one single decimal number
  Range 0 - 65535
  e.g. 80 – Web
  25 – SMTP
  4070 – Spotify

## Slide 15: Port Numbers
Internet Corporation for Assigned Names and Numbers (ICANN) assigns port numbers
Three categories:

## Slide 16: Port Number Types
Well-Known Ports:
  Assigned and controlled by IANA for standard services
  Commonly used by system processes and standardized services and applications.
143 – IMAP
110 – POP3
443 – HTTPS
53 - DNS
80 – HTTP
67&68 – DHCP
123 – NTP
25 – SMTP

## Slide 17: Port Number Types
Registered Ports:
  Assigned by IANA but for specific applications requested by developers or organizations.
  Can be registered for a lot of not-so-well-known, especially corporate/proprietary protocols.
23399 – Skype
8008 – Alternate HTTP
8080 – Alternate HTTP
4070 – Spotify
5060 – SIP (VoIP)
3306 – MySQL

## Slide 18: Port Number Types
Dynamic Ports:
  Also known as private or ephemeral ports
  Never assigned or controlled by IANA.
Dynamic port usage will become clearer as we move through the material.

## Slide 19: More on Port Numbers
Server is listening on Port 80 for HTTP connections.
The client sets the destination port to 80 and uses a dynamic port as its source.
Source = 49650 Destination = 80
Cisco.com Server

## Slide 20: Port Numbers in Action
Server replies with the web page.
  Sets the source port to 80 and uses the client’s source port as the destination.
Source = 80 Destination = 49650

## Slide 21: Port Numbers in Action
Source = 80 Destination = 49650
Source = 49650 Destination = 80
Clients can use any random port number, Servers can’t.
  Because clients won’t be able to identify server process otherwise
  Servers thus must use well-known port numbers!

## Slide 22: Port Numbers in Action
What if there are two sessions to the same server?
  The client uses another dynamic port as its source and the destination is still port 80.
  Different source ports keep the sessions unique on the server.
Source = 49650 Destination = 80
Source = 49655 Destination = 80
Source = 80 Destination = 49650
Source = 80 Destination = 49655
172.16.230.5
207.22.146.33

## Slide 23: Port Numbers in Action
Source = 49650 Destination = 80
Source = 49655 Destination = 80
Source = 80 Destination = 49650
Source = 80 Destination = 49655
172.16.230.5
207.22.146.33
There are two tabs in the same PC, then?
  The client uses another dynamic port as its source and the destination is still port 80.
  Different source ports keep the sessions unique.

## Slide 24: More on Port Numbers in Action
Source = 49650 Destination = 80
Source = 49650 Destination = 80
172.16.230.5
172.16.230.6
207.22.146.33
How does the Server’s Transport Layer keep them separate?
  The socket (IP Address:Port)
172.16.230.5:49650 172.16.230.6:49650
207.22.146.33:80 207.22.146.33:80

## Slide 25: Port Numbers in Action

## Slide 26: Port Addressing Types and Tools
TCP/UDP
Source IP
Source Port
Destination IP
Destination Port
Connection State
Source Socket
Destination Socket
netstat –a –n command
Netstat - Network Utility Tool

## Slide 27: Function 4 –Multiplexing
multiplexing
transport
application
Multiplexing

## Slide 28: Function 4 –DeMultiplexing
?
Demultiplexing
transport
application
Demultiplexing

## Slide 29: DeMultiplexing/ Multiplexing
Multiplexing, demultiplexing: based on segment, datagram header field values
UDP: demultiplexing using destination port number (only)
TCP: demultiplexing using 4-tuple: source and destination IP addresses, and port numbers

## Slide 30
IP & Port address,
As they are received

## Slide 31
I. Yes, the given range belongs to the dynamic port addresses class.
II. For long time use, the students should get the port registered for their server from ICANN.

## Slide 32: And Now more on TCP!