## Slide 1: Network Layer: IP Addressing
Lecture 6 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
IPv4 Address
  Structure
  Subnet/Prefix Mask
Types of IPv4 Address
IPv6 Address
  Structure

## Slide 3: Anatomy of IPv4

## Slide 4: Anatomy of an IPv4 Address
Each device on a network must be uniquely identified at the Network layer.
For IPv4, a 32 bit source and destination address is contained in each packet.

## Slide 5: IPv4 Addressing Structure

## Slide 6: Anatomy of an IPv4 Address
Dotted decimals
Network part
Host part
32 bits
Divided into 4 Octets

## Slide 7: Binary to decimal and Vice Versa

## Slide 8: Networks and Hosts
To identify a path or "route" through a network, the address must be composed of two parts:
  Network portion
  Host portion
1.1
1.2
1.3
2.1
2.2
3.1
3.2

## Slide 9: Network Portion
Network Portion:
  Some portion of the high-order bits
  A network can be defined as a group of hosts that have identical bit patterns in the network address portion of their addresses.
192.168.1.2 | 11000000 | 10101000 | 00000001 | 00000010
192.168.1.67 | 11000000 | 10101000 | 00000001 | 01000011
192.168.1.204 | 11000000 | 10101000 | 00000001 | 11001100

## Slide 10: Network Portion
Host Portion:
  A variable number of least significant bits that are called the host portion of the address.
  The number of bits used in this host portion determines the number of hosts that we can have within the network.
192.168.1.2 | 11000000 | 10101000 | 00000001 | 00000010
192.168.1.67 | 11000000 | 10101000 | 00000001 | 01000011
192.168.1.204 | 11000000 | 10101000 | 00000001 | 11001100

## Slide 11: Prefix Mask
How do we or devices identify the network part or the host part?
Answer: Using the “Prefix Mask”.
192.168.10.2/24
  Means that the first 24 bits are the network portion.
  The last 8 bits are the host portion.
Subnet Mask; the other form of “Prefix Mask”.
  Prefix length of /24 means a subnet mask of 255.255.255.0

## Slide 12: Subnet Mask
The Prefix Mask and the Subnet Mask are different ways of representing the same information.
Conversion:
  Subnet mask has the same format as an IP address. Hence, it has 32 bits divided into 8 bits (octets)
  Prefix mask of /24 means, the first (MSB) 24 bits of subnet mask would be 1 and the rest will be 0
  Binary: 11111111.11111111.11111111.00000000
Decimal: 255 . 255 . 255 . 0
Examples:
  Prefix Mask of /24
  Prefix Mask of /16
  Prefix Mask of /8
  or a subnet mask of 255.255.255.0
  or a subnet mask of 255.255.0.0
or a subnet mask of 255.0.0.0

## Slide 13: Exercise
What’s the subnet mask of the following?
  IP Address: 10.24.36.2 / 4
  IP Address: 10.24.36.2 / 12
  IP Address: 10.24.36.2 / 16
  IP Address: 10.24.36.2 / 23
What’s the prefix mask of the following?
  IP Address: 10.24.36.2; Subnet Mask: 255.255.224.0
  IP Address: 10.24.36.2; Subnet Mask: 255.255.255.192
  IP Address: 10.24.36.2; Subnet Mask: 255.255.255.252
  IP Address: 10.24.36.2; Subnet Mask: 255.254.0.0
  IP Address: 10.24.36.2; Subnet Mask: 255.255.240.0

## Slide 14: ANDing the Binaries
Inside data network devices, digital logic is applied for their interpretation of the addresses.
AND is used in determining the network address.
  0 AND 0 = 0
  1 AND 0 = 0
  1 AND 1 = 1
  0 AND 1 = 0
 | Decimal | Binary
IP Address | 135.15.2.1 | 10000111 00001111 00000010 00000001
Subnet Mask | 255.255.0.0 | 11111111 11111111 00000000 00000000
Network Address | 135.15.0.0 | 10000111 00001111 00000000 00000000

## Slide 15: But Why AND?
Routers use the ANDing process to determine the route a packet will take.
The network number of the destination IPv4 address is used to find the network in the routing table.
The router then determines the best path for the frame.

## Slide 16: IPv4 Addresses
Network Address
Host Address
Broadcast Address

## Slide 17: The Addresses
Network Address
  All hosts in the network will have the same network bits.
  Cannot be assigned to a device.
  All host bits in this address will be zero.
IP Address | 10. | 0. | 0. | 0
IP Address in Binary | 00001010 | 00000000 | 00000000 | 00000000
10.0.0.0/24
Network Part
Host Part
10.0.0.0/24

## Slide 18: The Addresses
Broadcast Address
  Used to send message to all hosts in the network using one single address
  Cannot be assigned to a device.
  All host bits in this address will be one.
IP Address | 10. | 0. | 0. | 255
IP Address in Binary | 00001010 | 00000000 | 00000000 | 11111111
10.0.0.255/24
Network Part
Host Part
Broadcast Address of 10.0.0.0/24 network is 10.0.0.255/24

## Slide 19: The Addresses
IP Address | 10. | 0. | 0. | 3
IP Address in Binary | 00001010 | 00000000 | 00000000 | 00000011
Host Address
  The unique address assigned to each device on the network.
  For a network of 10.0.0.0/24
    Addresses 10.0.0.1 through 10.0.0.254 are
    All host bits in this address will vary.
IP Address | 10. | 0. | 0. | 1
IP Address in Binary | 00001010 | 00000000 | 00000000 | 00000001
10.0.0.5/24
Network Part
Host Part
Host Address

## Slide 20: The Addresses
Say, you have a random IP address 192.168.10.193/24 or given as 192.168.10.193 255.255.255.0
Say, you have a random IP address 200.32.16.192/26 or given as 200.32.16.192 255.255.255.192

## Slide 21: Network Prefix
The network prefix is not always /24.

## Slide 22: Types of IPv4 Addresses

## Slide 23: Special Addresses

## Slide 24: Unicast
172.16.4.253 | 172.16.4.1 | Data
Dest IP Add | Source IP Add | Packet
Packet
Unicast
  A message to one host.
  Individual IPv4 addresses

## Slide 25: Broadcast
Limited Broadcast
  A message to all hosts on the same physical/local network or subnet.
  255.255.255.255
  Never forwarded by routers!
Packet
Packet
Packet
Packet
255.255.255.255 | 172.16.4.1 | Data
Dest IP Add | Source IP Add | Packet
Packet

## Slide 26: Broadcast
 | 172.16.4.1 | Data
Dest IP Add | Source IP Add | Packet
Packet
200.20.10.255
Packet
Packet
Packet
Packet
Packet
Packet
Directed Broadcast
  A message to all hosts on a different network or subnet.
  broadcast address of a network
  Example : 200.20.10.255

## Slide 27: Multicast
Packet
Packet
Packet
224.10.10.5 | 172.16.4.1 | Data
Dest IP Add | Source IP Add | Packet
Multicast Addresses
  A message addressed to a group of hosts.
  Uses an IP address starting within this range of 224 - 239
Examples of Multicast Application
  Video and audio broadcasts
  Distribution of software
  News feeds

## Slide 28: Loopback
Loopback Address
  A message addressed to loop back in the device itself.
  127.x.x.x of 127.0.0.0/8
  Not assigned to any device
  Testing and Troubleshooting purpose
Packet
127.0.0.1 | 172.16.4.1 | Data
Dest IP Add | Source IP Add | Packet
Notes: It allows applications to communicate with each other within the same host without requiring physical network hardware or connectivity.
The loopback address is often used for troubleshooting network issues, testing server applications, or ensuring that network software is functioning as expected locally.
Characteristics: Packets sent to a loopback address never leave the host device; they are routed internally, ensuring no external network traffic is involved.

## Slide 29: Anatomy of IPv6 Address

## Slide 30: Reasons for using IPv6
Address Availability:
  IPv4: 32 bits - 4 octets
    2^32 or 4,294,467,295 IP Addresses.
  IPv6: 128 bits - 16 octets
    2^32
    3.4 x 10^38 or
  340,282,366,920,938,463,463,374,607,431,768,211,456
  (340 undecillion) IP Addresses.
Every grain of sand on every beach on Earth could be assigned over a million unique IPv6 addresses, with plenty to spare (assuming approximately 7.5 x 10^18 grains of sand globally and 2^128 IPv6 addresses).

## Slide 31: IPv6 Address
128 bits
given below is a 128 bit IPv6 address represented in binary format and divided into eight 16-bits blocks
Each 4 bits is converted into a Hexadecimal digit
Each block contains 4 Hexadecimal digits
Each block is separated by ‘:’ symbol

## Slide 32
IPv6 Address
Called string notation
2
0
0
1

## Slide 33: IPv6 Address
Notes: This is just for the students

## Slide 34: IPv6 Addressing
IPv6 Representation – Rule 1:
  The leading zeros in any 16-bit segment do not have to be written. If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeros.
130B

## Slide 35: IPv6 Addressing
IPv6 Representation – Rule 2:
  Any single, contiguous string of one or more 16-bit segments consisting of all zeroes can be represented once with a double colon.
1080:0:0:0:8:800:200C:417A | = | 1080::8:800:200C:417A
FF01:0:0:0:0:0:0:101 | = | FF01::101
0:0:0:0:0:0:0:1 | = | ::1
0:0:0:0:0:0:0:0 | = | ::
17

## Slide 36: IPv6 Addressing
IPv6 Representation – Rule 2:
  Any single, contiguous string of one or more 16-bit segments consisting of all zeroes can be represented once with a double colon.
Example: 1843::22::fa
  Illegal because the length of the two all-zero strings is ambiguous.
  1843:0000:0000:0000:0022:0000:0000:00fa
  1843:0000:0000:0022:0000:0000:0000:00fa
or
18

## Slide 37
Representing IPv6 addresses
No Subnet masks in dotted decimal format in IPv6
IPv4 Address
IPv6 Address

## Slide 38: The End