## Slide 1: Objectives
Short overview of the Network Layer
Packet Switching: Virtual Circuits & Datagram Networks
IPv4 Packet Format
IP Fragmentation & Reassembly
ICMP
  Ping
  Traceroute

## Slide 2: The Network Layer
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
Encapsulates data into packets on the sending side.
Network Layer protocols operates on hosts and routers.
Routers inspect IP header fields for forwarding.
Delivers segments to the transport layer on the receiving side.

## Slide 3: Packet Switching
Notes: Data Communications and Networking. Behrouz A. Forouzan
Section 18.2

## Slide 4: Packet Switching
Packet Switching is a method of transferring data across a network by breaking it into smaller packets.
Two type of networks based on packet switching
  Datagram Networks
  Virtual Circuit Networks

## Slide 5: Datagram networks
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data
No Call Setup:
    Devices can send data immediately without establishing a connection.
Stateless Routers:
Routers forward packets independently based on their destination IP address.
Packet Forwarding:
Packets from the same source may take different paths to reach the destination.
Notes: Each router does not maintain information about previously forwarded packets.

## Slide 6: Virtual Circuits: Signaling Protocols
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data
Call Setup:
    A connection (virtual circuit) is established between sender and receiver before data transfer.
Stateful Routers:
Routers maintain information about active connections (virtual circuits).
Packet Forwarding:
All packets follow the same path through the network.
Notes: Example:
Asynchronous Transfer Mode (ATM) or MPLS (Multiprotocol Label Switching) networks.

## Slide 7: Network Layer: IPv4 Functions
Lecture 9 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 8: Functions of Network Layer
Routing:
Finds the best path from source → destination
Done by routing algorithms
Analogy: planning a trip before you travel
Forwarding:
move packets from router’s input to appropriate router output
Analogy: process of getting through a single interchange
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 9: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 10: Control Plane – the brain!
Control plane builds the routing table using routing protocols.
It creates the forwarding table FIB (Forwarding Information Base), a simplified version of routing table.
The FIB may be created using
  simple destination-based rules
  or more advanced generalized rules.
Control plane installs this FIB into every input port.
Decentralized Switching

## Slide 11: Data Plane – the hands and legs!
How input ports use the FIB?
Forwarding rules can be:
  Destination-based forwarding :
    Uses only destination IP to choose output port
    If destination = 200.20.20.0/24 → send to port s0/0/0.
  Generalized forwarding :
    Admins can add multiple header fields (IP, protocol, port, etc.) Or special rules (QoS)
    If video packet (UDP, port 5000) → high-priority queue.
These rules are stored in the FIB created by the control plane

## Slide 12: Input port functions
switch
fabric
line
termination
physical layer:
Converts signal → digital bits
link
layer
protocol
(receive)
link layer:
Removes data link header/trailer
Checks for errors
Extracts the IP packet
Frame
lookup,
forwarding
queueing
Notes: Green box is a physical layer responsible for receiving bit level transmission. Copper, fiber wireless.
Link layer in blue – bit assemble into Ethernet frame. We will discuss this in details in chapter 6.
But most critical one, is here. Lookup, forwarding function. Lookup and forward is “Match plus action” behavior.
GOAL – processing at “line speed”, otherwise, buffer will be full and packet will be lost

## Slide 13: Input port functions
line
termination
lookup,
forwarding
queueing
Network layer:
Input port checks packet header
Matches against local FIB copy
Decides output port (using destination-based or generalized rule)
switch
fabric
link
layer
protocol
(receive)
Datagram or packet
Input Port Queueing
If packets arrive too fast → they wait here
If queue is full → packet is dropped

## Slide 14: Internet Protocol IPv4

## Slide 15: Internet Network Layer
Host, router network layer functions:
forwarding
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 16: IPv4 Datagram Format
The size of an IP datagram:
The minimum size is 20 bytes (if you have no data)
The maximum size is 65,535 bytes
Notes: 19.1.1 Datagram Format (Data Communications and Networking. Behrouz A. Forouzan)

## Slide 17: IPv4 Datagram Header Format
Version: value of which IP version is being used. For IPv4 the value will be 4 here.
Internet Header Length: value of the header length, min 20 bytes, max 60 bytes. Shown in 4 byte word. So min value 5, max 15.
Type of Service: for QoS (Quality of Service). To mark the packet to give special treatment or priority.
Total Length: value of the entire size of the IP packet (header and data) in bytes.
Notes: 19.1.1 Datagram Format (Data Communications and Networking. Behrouz A. Forouzan)

## Slide 18: IPv4 Datagram Header Format
Time to Live: maximum number of hops (routers) a packet can travel
Protocol: value tells us which upper layer protocol is present, for example TCP has value 6 and UDP has value 17.
Header Checksum: to check if there are any errors in the header.
Options: value of any extra information. Options are rarely used now.
Padding:
Used only when Options are present. Ensures the header length becomes a multiple of 4 bytes
Notes: 19.1.1 Datagram Format (Data Communications and Networking. Behrouz A. Forouzan)

## Slide 19: Time to Live - TTL
Maximum number of hops (routers) a packet can traverse before being discarded.
At each hop, the TTL is decreased by 1.
When the TTL reaches 0, the packet is dropped.
And an error message is sent back to the sender.

## Slide 20: Time to Live - TTL
TTL=64
TTL=64
TTL=63
TTL=62
TTL=61
TTL=60
TTL=60
TTL=59
Not just the "value of hops“
It's a mechanism to prevent packets from looping endlessly in the network.
Ensure finite packet lifetimes.

## Slide 21: IPv4 Datagram Format
Notes: 19.1.1 Datagram Format (Data Communications and Networking. Behrouz A. Forouzan)

## Slide 22: IP Fragmentation & Reassembly
Network links have MTU
  Maximum transmission unit or maximum transfer size
  Different link types have different MTUs
fragmentation:
in: one large datagram (4000 bytes)
out: 3 smaller datagrams
reassembly
Link MTU: 1500bytes

## Slide 23: IP Fragmentation & Reassembly
MTU=1500 => 20(H)+1480(D)
1st fragment : 5120-1480=3640
Data 5140=> 20(H)+5120(D)
Last/4th Segment : 680+20=700
1st / start byte number
2nd fragment : 3640-1480=2160
3rd fragment : 2160-1480=680
Notes: Another example – for students to work out

## Slide 24: IP Fragmentation & Reassembly
offset
=0
One large datagram becomes
several smaller datagrams
1480 bytes in data field
Example:
  4000 Bytes of datagram
  MTU = 1500 Bytes
DF – Don’t Fragment Bit
  Value 0 or 1
length
=1500
ID
=122
MF
=1
DF
=0
ID
=122
offset
=0
MF
=0
length
=4000
DF
=0
length
=1500
ID
=122
DF
=0
MF
=1
offset
=185
offset = 1480/8
length
=1040
ID
=122
DF
=0
MF
=0
offset
=370
offset = 2960/8
Fragment Offset
    The value of the offset is measured in units of 8 bytes.
Extra Example
Notes:     The value of the offset is measured in units of 8 bytes.
    This is done because the length of the offset field is only 13 bits long and cannot represent a sequence of bytes greater than 8191.
    This forces hosts or routers that fragment datagrams to choose the size of each fragment so that the first byte number is divisible by 8.

## Slide 25: A packet of size 2584 bytes including 32 bytes of header was fragmented for transmitting in a link with MTU=X bytes. The 9th packet has a size of 272 bytes. It also has its MF bit set. I. Calculate the value of X. II. Calculate the fragment offset for the 7th packet. III. Find out the total number of fragmented packets
Total data size: packet size-header size=2584-32=2552 bytes
MTU size, X= 272 bytes
Data size per fragment= 272-32=240 bytes
FORMULA:

## Slide 26: A packet of size 7240 bytes including 40 bytes of header arrived at a router. The router can send at most 800 bytes at a time through the link and thus fragment accordingly. I. Calculate the number of fragments that will be created. II. Calculate the fragment size of the last fragment. III. Calculate the fragment offset of the 8th fragment. IV. Explain why the MF bit is always zero for the last fragment.

## Slide 27: ICMP
Internet Control Message Protocol

## Slide 28: ICMP
It helps devices send error messages and status updates.
Functions:
  Reporting errors in the network
  Checking reachability (Is the host alive?)
  Diagnosing delays and congestion
Key Points:
  ICMP does not carry actual user data
  Mainly used by the operating systems for network management
Example of ICMP in practice
  Ping
  Traceroute

## Slide 29: Ping
Packet Internet Groper and is a network utility tool.
Purpose:
      Checks if a device is reachable
      Measures the time it takes for data to travel (round-trip time).
    Mechanism:
    Sends ICMP Echo Request packets
    Receives Echo Reply packets.
    Results:
    Displays the number of packets sent/received/lost
    The time taken(delay).
Commands: ping 216.58.200.174

## Slide 30: Ping
Questions :
              Why 4 replies?
              What the time refer to?
              What is the TTL refer to?
Notes: TTL is 114, which means that the original TTL value (commonly 128 or 255 depending on the operating system) was decremented by 14 during the journey. This suggests the packet passed through 14 routers. Why it matters: The TTL value in the ping response indicates how many hops remained before reaching your device. It can give an indirect idea of how far (in terms of network hops) the target is. represents the round-trip time it takes for an ICMP echo request to travel from your device to the target It indicates the latency or delay in the network connection. Lower values mean faster responses and better network performance.Example in the output: The times vary slightly, such as 36ms, 37ms, and 38ms, showing minor variations in network latency.

## Slide 31: ICMP Packet Format
IP Header 20 bytes | IP Payload/ Data
ICMP Header 8 bytes | ICMP Data (variable)

## Slide 32: ICMP Packet Format

## Slide 33: Unsuccessful Ping

## Slide 34: Ping Attacks
ICMP DDOS attack – Zombie Attack:
Notes:   Much like the ping flood method, only multiple computers are being used.
  In this instance, the computers that are being used may or may not be aware of the fact that they are attacking a website or network.
  Trojans and viruses commonly give the hacker control of a computer, and thus, the ability to use them for attack. In this case the victim computers are called zombies.

## Slide 35: Ping Attacks
ICMP DDOS attack – Packet magnification (or ICMP Smurf):
Notes: An attacker sends forged ICMP echo packets to vulnerable networks' broadcast addresses. All the systems on those networks send ICMP echo replies to the victim. Prevention: Disable ICMP Echo Requests: Configure firewalls or routers to block incoming ICMP packets, especially "Echo Request" packets, to prevent attackers from exploiting ping.
Use Rate Limiting: Limit the number of ICMP packets a device or network can process per second, reducing the impact of flood attacks.
Prevent IP Spoofing:

## Slide 36: IP MTU Discovery with ICMP
MTU = 4000
host
host
router
MTU = 1500
MTU = 2000
IP
Packet
Length = 4000, Don’t Fragment
router
Sends ICMP
Frag. Needed
MTU = 2000
Router drops the packet and
4000

## Slide 37: IP MTU Discovery with ICMP
MTU = 4000
host
host
router
MTU = 1500
MTU = 2000
IP
Packet
Length = 2000, Don’t Fragment
router
Sends ICMP
Frag. Needed
MTU = 1500
Router drops the packet and
2000
2000

## Slide 38: IP MTU Discovery with ICMP
MTU = 4000
host
host
router
MTU = 1500
MTU = 2000
IP
Packet
Length = 1500, Don’t Fragment
router
  When successful, no reply at IP level
    “No news is good news”
    Higher level protocol might have some form of acknowledgement

## Slide 39: Traceroute
Shows the path your packets take through different routers to reach a destination.
Purpose:
  Identifies the routers or hops data passes through to reach its destination mostly for troubleshooting
Mechanism:
  Sends ICMP packets with TTL = 1, 2, 3…
  Each router where TTL becomes 0 sends ICMP Time Exceeded
  Traceroute uses these replies to list each hop in order

## Slide 40: Traceroute

## Slide 41: Traceroute
Commands:
  Unix: traceroute
  Cisco IOS: traceroute (trace)
  DOS: tracert
Results The IP or hostname of every hop and the time each hop takes (latency)

## Slide 42: Using Tracert
Hop 1: Our local router or gateway (private IP address).
Hops 2–5: Internal routing within Bracu ISP's private network (non-public IPs).
Hop 6: First public IP, ISP's gateway to the internet.
Hops 7–9: Routing through regional and backbone ISPs.
Hops 10–13: Routing through Singapore (a major internet hub).
Hops 14–19: Routing through Indian networks, ending in Mumbai.
Hop 20: Final destination—Yahoo's server, located in India, near Mumbai.

## Slide 43: Traceroute: Another example
Hop 1: User LAN router
Hops 2-4: Verizon network (a backbone ISP)
Hops 5-6: Alternet (a backbone ISP)
Hops 7-11: Level 3 (a backbone ISP)
Hops 12-14: the Google LAN

## Slide 44: Traceroute: Request Timed Out
This message indicates that the router security settings keep it from revealing its identity or the router and connection are slow.

## Slide 45: The End